## Slide 1: Receive CPU Selection Framework
Cross-Layer Optimization In Network Stack to Improve Server Scalability
Jiaquan He
School of Software
Tsinghua University
Beijing, China
objectkuan@gmail.com
Yu Chen
Department of Computer
Science and Technology
Tsinghua University
Beijing, China
yuchen@mail.tsinghua.edu.cn
Yong Zhang
Department of Computer
Science and Technology
Tsinghua University
Beijing, China
zhangyong05@tsinghua.edu.cn
Chunxiao Xing
Department of Computer
Science and Technology
Tsinghua University
Beijing, China
xingcx@tsinghua.edu.cn

## Slide 2: Outline
Introduction
Related Work
Web Request in the Network Stack
Alternatives and Problems
Method and Architecture
Experiments
Future work
Conclusion
Acknowledgement

## Slide 3: Introduction
Hardware
CPU
Memory
IO
OS
Applications
httpd
haproxy
redis
WinServer
Linux
++

## Slide 4: Introduction
Scalability
Hardware
CPU
Memory
IO
OS
Applications
httpd
haproxy
redis
WinServer
Linux
++

## Slide 5: Introduction
Scalability
  Multi-thread mode - Memcached
  Multi-process mode - Nginx
  Multi-instance mode - Redis
Why not scale well
  Share heaps, global variables, etc.
  Share master processes.
  Share hardware resources.
Thread/Process/Instance++
Performance++

## Slide 6: Introduction
Scalability – CPU binding
Hardware
CPU0
CPU1
CPUn
OS
Applications
pid0
pid1
pidn
WinServer
Linux
…
…

## Slide 7: Related Work
Server application
  Dias, Daniel M., et al. "A scalable and highly available web server."Compcon'96.'Technologies for the Information Superhighway'Digest of Papers. IEEE, 1996.
  Tao, Kang, et al. "A Multi-Tenant Level Lightweight Lock Mechanism for Multi-Tenant Database", Web Information Systems and Applications Conference (WISA), 2014 Ninth. IEEE, 2014.
Network stack
  Pesterev, Aleksey, et al. "Improving network connection locality on multicore systems." Proceedings of the 7th ACM european conference on Computer Systems. ACM, 2012.
  Jeong, E., et al. "mTCP: a highly scalable user-level TCP stack for multicore systems." Proc. 11th USENIX NSDI (2014).
  Han, Sangjin, et al. "MegaPipe: A New Programming Interface for Scalable Network I/O." OSDI. 2012.
Others
  Lim, Hyeontaek, et al. "MICA: A holistic approach to fast in-memory key-value storage." management 15.32 (2014): 36.
  Veal, Bryan, and Annie Foong. "Performance scalability of a multi-core web server." Proceedings of the 3rd ACM/IEEE Symposium on Architecture for networking and communications systems. ACM, 2007.
Notes: 1 The system architecture consists of a set of logical front-end or network nodes and a set of back-end or data nodes connected by a switch, and a load balancing component. A combination of TCP routing and Domain Name Server (DNS) techniques are used t o balance the load across the front-end nodes that run the Web (httpd) daemons.

## Slide 8: Related Work
Server application
  New server software
Network stack
  New API
DO NOT FIT PRODUCTION ENVIRONMENT

## Slide 9: Web Request in the Network Stack

## Slide 10: Web Request in the Network Stack
Notes: STEP 1. When a packet arrives at the NIC. It is dispatched to one of the receive queues inside the NIC according to the NIC configuration. Each receive queue is usually bound to a CPU core so that packets in that queue are always processed within one CPU core, in order to avoid cache misses and CPU switches (which is also known as connection locality).
STEP 2. At regular time intervals, the NIC triggers an interrupt to the operating sytem, and the NIC driver polls the receive queue, reads the packets and stores its contents in a sk_buff structure. If some software load balancing features (e.g. RFS) are enabled, the packet will be put in a certain CPU core according to its quintuple (source IP, source port, destination IP, destination port, transport layer protocol). Otherwise it will be processed simply on the IP layer.
STEP 3. The IP layer function is called to process the packet, and extract its routing information. If this computer is the destination of the packet, it will stay. Otherwise, it will be forwarded out.
STEP 4. Many web requests take TCP as the transport layer protocol. The TCP layer extracts the TCP header of a packet, deals with the packet’s connection state and transport sequence. It determines which socket matches the packet and the packet is finally put in the receive queue of that socket.
STEP 5. The data receiving process of the web server applications calls socket-related functions to receive the data, and the data are then copied from the kernel space to the user space.

## Slide 11: Alternatives and Problems
Hardware
  RSS (Receive-Side Scaling)
  NTUPLE
  ATR (Application Target Routing)
Software
  RPS (Receive Packet Steering)
  RFS (Receive FlowSteering)
<source ip, source port, protocol, dest ip, dest port> → CPU
Notes:     RPS RFS Tom Herbert

## Slide 12: Method And Architecture
RCS (Receive CPU Selection)

## Slide 13: Method And Architecture
RCS (Receive CPU Selection)
  Direct TCP
  CPU Selection

## Slide 14: Method And Architecture
RCS (Receive CPU Selection) – Direct TCP

## Slide 15: Method And Architecture
RCS (Receive CPU Selection) – CPU Selection
C1
C2
C3
Connection Locality
Notes: Soon after the packet arrives, it is put in a NIC receive queue, which is processed later by a CPU core C1.
After the packet enters the network stack and before it leaves for the IP layer, if RPS or RFS is enabled, the packet will be put to a packet queue residing on a CPU core C2.
The packet is finally copied from the kernel space to the web server process in the user space, which may be running on a CPU core C3.

## Slide 16: Method And Architecture
RCS (Receive CPU Selection) – CPU Selection
Notes: Packet Sending:
A request is sent out by the web server through the socket.
The CPU Selection feature stores the current CPU core in the sock structure.
The packet is sent out as normal.
2)Packet Receiving:
④A packet arrives at the NIC and is passed to an sk_buff structure.
⑤The CPU Selection feature scans one of the TCP tables (taking the established table for example). It finds the sock structure that matches the packet.
⑥From the sock structure, the network stack is now aware of the target CPU core, so it can then put the packet to the packet queue of a proper core.
⑦The sock structure is then cached in sk_buff, and when a packet of the same connection comes next time, the network stack does not need to scan the tables again.

## Slide 17: Method And Architecture
Deployment
  Build a patched Linux kernel (now support kernels for CentOS 6.4/6.5)
  LD_PRELOAD=./libfsocket.so ./redis-server

## Slide 18: Experiments
CPU0
CPU11
…
Redis0
Redis1
…
Server
CPU0
CPU11
…
BM0
BM1
…
Client0
CPU0
CPU11
…
BM0
BM11
…
Client1

## Slide 19: Experiments
Redis servers on a node with 12 CPU cores of Intel(R) Xeon(R) CPU E592620 0 @ 2.00GHz, 48GB RAM and NIC of Intel Corporation 82599ES 109Gigabit SFI/SFP+ Network Connection
Benchmarks on two separate nodes.
  Client node 1 has 12 CPU cores with Intel(R) Xeon(R) CPU E592640 0 @ 2.50GHz, with 48GB RAM, and NIC of Intel Corporation 82599ES 109Gigabit SFI/SFP+ Network Connection.
  Client node 2 has 16 Genuine Intel(R) CPU @ 2.70GHz, with 16GB RAM, and NIC of Intel Corporation 82599EB 109Gigabit SFI/SFP+ Network Connection.

## Slide 20: Experiments
Hardware | No-Optimization | RCS Enabled
RSS | 932490.246639 | 1006164.57254
ATR | 1158842.82151 | 1195729.99134
NTUPLE | 1199302.39639 | 1190293.1895
Notes: 12个Redis实例，benchmark对每个实例500并发，43+60压44

## Slide 21: Experiments
Chart: Amount of Redis Instances
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0
RSS | 100234 | 199899 | 292932 | 385965 | 462559.25 | 539153.5 | 615747.75 | 692342 | 752379.0617 | 812416.1233 | 872453.185 | 932490.2466
RFS | 100734 | 200023 | 296667.5 | 393312 | 477569.5 | 561827 | 646084.5 | 730342 | 788079.75 | 845817.5 | 903555.25 | 961293
RCS | 101234 | 200312 | 304796.5 | 409281 | 500238.75 | 591196.5 | 682154.25 | 773112 | 831375.1431 | 889638.2863 | 947901.4294 | 1006164.5725
Performance differences of RSS, RFS, and RCS
Notes: 1 100234 100734 101234
2 199899 200023 200312
4 385965 393312 409281
8 692342 730342 773112
12 932490 961293 1006164

## Slide 22: Conclusion
Propose RCS
  Scalability improvement
  No modification to software source
  Independence of hardware
  Good fit for production environment

## Slide 23: Future work
Application on more scenes
Compatible with more OS platforms

## Slide 24: Acknowledgement
Sponsored by:
  National Science and Technology Major Project of China 2012ZX01039-004
  National Science and Technology Major Project of China 2013ZX01039001-002
With help from:
  Xiaodong Li @ Sina
  Xiaofeng Lin @ Zhihu
Source code:
  Fastsocket: https://github.com/fastos/fastsocket

## Slide 25: The End
Thank you.
Jiaquan He
OS Center, RIIT, Tsinghua University